## Slide 1
NN Kernels
Sergio Zerpa
DES SDF FW

## Slide 2: Content
AIFORDES Overview
TensorFlow Lite for Microcontrollers (TFL Micro)
TFL Micro
  Components
  Software architecture
  Development flow
  Trained model
    Quantization
TFL Micro – NN Kernels optimizations
CMSIS NN –
  Overview
  Integration with TFL micro
  An alternative approach for RiscV?
More info

## Slide 3: Overview: AIFORDES workflow
Next step:
Run on
Embedded
Target
(Inference)

## Slide 4: Overview: Neural networks
y1
y2
y3
y4
x1
x2
x3
x4
Training: structure of network (interconnections, nodes, weights, etc.)
  Main challenge:
    Generation of optimized models
    Accuracy of output
Inference: calculating output for a given input
  Main challenge:
    Number of arithmetic operations
    Restricted memory for model and calculations

## Slide 5: Tensor Flow Lite for Microcontrollers (TFL Micro)
Training/generating a model
Running inference

## Slide 6: TFL Micro – Components
Focus: The interpreter performs inference to compute the output for new-inputs. It uses NN Kernels such as:
Fully-connected layers
Convolution layers
Pooling layers
Softmax-layers
Source-code: aiml_deployment\tensorflow\tensorflow\lite\micro
Load
Trained-model
Init
Prepare
Eval
Invoke (after setting new input)
Peripheral X
Main Processor
Trained-model loader
Peripheral X
Driver
Input generator
Operations Resolver
Error reporter
Micro
Interpreter
Output handler
Peripheral Y
Driver
Peripheral Z
Driver
Reference kernel
*Platform kernel
Math
(standard lib)
NN-Math
Peripheral Y
Peripheral Z
The interpreter sequence:
The Model:
The interpreter:

## Slide 7: TFL Micro - Software architecture (Block diagram)
Peripheral X
Main Processor
Trained-model loader
Peripheral X
Driver
Input generator
Operations Resolver
Error reporter
Micro
Interpreter
Output handler
Peripheral Y
Driver
Peripheral Z
Driver
Reference kernel
*Platform kernel
Math
(standard lib)
NN-Math
Peripheral Y
Peripheral Z
*Platform kernel: e.g. CMSIS-NN, optimized versions in TFL, etc.

## Slide 8: TFL Micro - Software architecture (Organizational diagram )
Main
Micro Interpreter
Operations resolver
Reference kernel
Platform kernel
Math (standard lib)
NN-Math
Generated model loader
Input generator
Output handler
Error
reporter
Peripheral X
Driver
Peripheral Y
Driver
Peripheral Z
Driver

## Slide 9: TFL Micro – Software architecture (Layered diagram)
Micro Interpreter
Operations resolver
Reference kernel
Platform kernel
Math
(standard lib)
NN-Math
Generated model loader
Input generator
Output handler
Error
reporter
Peripheral Y
Driver
Peripheral X
Driver
Peripheral Z
Driver
Application

## Slide 10: TFL Micro – Development flow (for Host computer)
TensorFlowLite Micro
Microcontroller-device
(e.g. platform includes, linker)
ML application with trained-model
Micro Interpreter
Operations resolver
Reference kernel
Math
(standard lib)
Kernel
(Interface)
Host
Development flow for host
Builder
Build-Scripts
Compiler
(gcc)
Executable
(.exe)
Debugger
(gdb)
Host
Computer

## Slide 11: TFL Micro – Development flow (for RiscV ISS)
TensorFlowLite Micro
Microcontroller-device
(e.g. platform includes, linker)
Development flow for Riscv
Builder
Build-Scripts
Compiler
(riscv)
Executable
(.elf)
Debugger
(gdb-client)
Target
Debugger
(gdb-server)
ISS
(SweRV)
ML application with trained-model
Micro Interpreter
Operations resolver
Reference kernel
Math
(standard lib)
Kernel
(Interface)
Microcontroller device
(RiscV)
Optimized kernel for RiscV
Math-nn
RiscV
Relies on TensorFlowLite-Micro acceptance tests (At interpreter level, and at kernel-level)
Builds within TensorFlowLite-environment

## Slide 12: TFL Micro - Trained model
Floating point model
  All weights are floating point value
  More accurate
  Required more hardware resources during inference
    Simpler arithmetic but more resources
Quantized model
  All weights are quantized integer values (32-bits, 16-bits, 8-bits or less)
  Less accurate
  Required quantization aware training techniques
  Required less hardware resources during inference
    Arithmetic that requires optimize-ways of doing operations but less resources
y1
y2
y3
y4
x1
x2
x3
x4

## Slide 13: TFL Micro - Trained model (Asymmetric quantization)
https://nervanasystems.github.io/distiller/algo_quantization.html
Quantization:
real value = (quantized value + zero point) / scale
xf : real value
qx: scale
xq: quantized_value
zpx : zero point
xf = (xq + zpx) / qx

## Slide 14: TFL Micro - Trained model (Asymmetric quantization)
e.g Converting a number back and forwards:
1.0f -> quantized_value = (real_value * scale) - zeroPoint = (1.0 * 2.0 ) – (-127) = 129
129 -> real_value = (quantized_value + zeroPoint) / scale = (129 + (-127)) / 2.0 = 1.0f
min = -63.5f
max = 64.0f
0.0f
Conver float to quantized-uint8:
scale = (2^n – 1) / (max – min) = 2.0f
zeroPoint = min * scale = -127
quantized_value = (real_value * scale) - zeroPoint
127
0
255
129
1.0f
125
-1.0f
Convert a quantized-uint8 back to float:
real_value ~= (quantized_value + zeroPoint) / scale
Quantization - From Float to quantized uint8

## Slide 15: TFL Micro - Trained model (Asymmetric quantization)
e.g Converting a number back and forwards:
1.0f -> quantized_value = (real_value * scale) - zeroPoint = (1.0 * 2.0) - 1 = 1
1 -> real_value = (quantized_value + zeroPoint) / scale = (1 + 1) / 2.0 = 1.0f
min = -63.5f
max = 64.0f
0.0f
Conver float to quantized-int8:
scale = (2^n – 1) / (max – min) = 2.0f
zeroPoint = abs(-128) + min * scale = 1
quantized_value = (real_value * scale) - zeroPoint
-1
-128
127
1
1.0f
-3
-1.0f
Convert a quantized-int8 back to float:
real_value ~= (quantized_value + zeroPoint) / scale
Quantization - From Float to quantized int8
2
1.5f
3
2.0f

## Slide 16: TFL Micro - Trained model (Quantization arithmetic)
min
max
0.0f
zeroPoint
min
max
a
Consider float values:
a_f, b_f , c_f
Consider its quantized values:
a, b, c
Consider scales A, B and C:
scale_a (Qa), zeroPoint_a (ZPa)
scale_b (Qb), zeroPoint_b (ZPb)
scale_c (Qc), zeroPoint_c (ZPc)
a_f
Then the float-multiplication can be expressed as:
c_f = a_f * b_f
The associated quantized-multiplication can be expressed as:
Therefore:
Or:
where
A: is an integer multiplier
n: number of bits to shift after multiplication

## Slide 17: TFL Micro - Trained model (Quantization scaling factor)
https://nervanasystems.github.io/distiller/algo_quantization.html

## Slide 18: TFL Micro - Trained model (Symmetric quantization)
https://nervanasystems.github.io/distiller/algo_quantization.html

## Slide 19: TFL Micro – NN Kernels optimizations Option 1
Peripheral X
Main Processor
Trained-model loader
Peripheral X
Driver
Input generator
Operations Resolver
Error reporter
Micro
Interpreter
Output handler
Peripheral Y
Driver
Peripheral Z
Driver
Reference kernel
*Platform kernel
Math
(standard lib)
NN-Math
Peripheral Y
Peripheral Z
Micro Interpreter
Operations resolver
Reference kernel
Math
(standard lib)
Kernel
(Interface)
Microcontroller device
Optimized kernel
Optimized
Math-nn
Load
Trained-model
Init
Prepare
Eval
Invoke
(after setting new input)
Take advantage of the interpreter‘s Prepare phase to pre-compute factors that depend only on the model and not on the new input.
  Prepare:
    Pre-calculate factors that only depend on the weights and biases in the model
    Allocate memory to store those factors (i.e. this requires extra-memory resources)
  Inference:
    Calculate factors that depend on new-input
    Combine results with the pre-computed factors
Can be pre-computed,
If value b comes with the model

## Slide 20: TFL Micro – NN Kernels optimizations Option 2
Peripheral X
Main Processor
Trained-model loader
Peripheral X
Driver
Input generator
Operations Resolver
Error reporter
Micro
Interpreter
Output handler
Peripheral Y
Driver
Peripheral Z
Driver
Reference kernel
*Platform kernel
Math
(standard lib)
NN-Math
Peripheral Y
Peripheral Z
Micro Interpreter
Operations resolver
Reference kernel
Math
(standard lib)
Kernel
(Interface)
Microcontroller device
Optimized kernel
Optimized
Math-nn
Introduce an offline-interpreter to pre-compute factors that depend only on the model and not on the new input.
  Offline:
    Pre-calculate factors that only depend on the weights and biases in the model
    Store those factors as meta-data which shall be provide it together with the model.
    Extend the interpreter kernel operations to correctly interpret the meta data
  Inference:
    Perform the operation accordingly, using the model, meta data and new input data.
Load
Trained-model
Init
Prepare
Eval
Invoke
(after setting new input)

## Slide 21: TFL Micro – NN Kernels optimizations Option 3
Peripheral X
Main Processor
Trained-model loader
Peripheral X
Driver
Input generator
Operations Resolver
Error reporter
Micro
Interpreter
Output handler
Peripheral Y
Driver
Peripheral Z
Driver
Reference kernel
*Platform kernel
Math
(standard lib)
NN-Math
Peripheral Y
Peripheral Z
Micro Interpreter
Operations resolver
Reference kernel
Math
(standard lib)
Kernel
(Interface)
Microcontroller device
Optimized kernel
Optimized
Math-nn
Take advantage of the sparsity of the matrices in the model, which requires:
  Introduce a variant of the kernel-operations to operate on sparse-inputs and sparse-weights
  Extend the interpreter kernel operations to correctly interpret the sparse-data and perform the operation accoridinly
Load
Trained-model
Init
Prepare
Eval
Invoke
(after setting new input)

## Slide 22: TFL Micro – NN Kernels optimizations Option 4
Adding enhancements in Hardware to perform kernel operations efficiently
  Vector instructions to accelerate matrix-vector operations
Peripheral X
Main Processor
Trained-model loader
Peripheral X
Driver
Input generator
Operations Resolver
Error reporter
Micro
Interpreter
Output handler
Peripheral Y
Driver
Peripheral Z
Driver
Reference kernel
*Platform kernel
Math
(standard lib)
NN-Math
Peripheral Y
Peripheral Z
Micro Interpreter
Operations resolver
Reference kernel
Math
(standard lib)
Kernel
(Interface)
Microcontroller device
Optimized kernel
Optimized
Math-nn
Load
Trained-model
Init
Prepare
Eval
Invoke
(after setting new input)!

## Slide 23: CMSIS-NN - Overview
The Model:
The Interpreter:
The Arm platform:

## Slide 24: CMSIS-NN – Overview (Dependencies on CMSIS-CORE)
CMSIS-NN functions are declared in arm_nnfunctions.h
CMSIS-DSP functions are declared in arm_math.h
  arm_math.h also includes the data-types use in arm_nnfunctions.h
CMSIS-DSP could be compile as an standalone library if we provide an implementation for the functions in arm_math that it uses.
arm_nnfunctions.h
arm_math.h
Arm Cortex processor

## Slide 25: CMSIS-NN - Overview (Performance)
Runtime using Kernels optimized for ARM micros:
Baselie runtime (using ARM non-optimized NN Kernels):

## Slide 26: CMSIS-NN - Integration with TFL micro
TensorFlowLite Micro
Microcontroller-device (e.g. platform includes, linker)
Wrapping TFLu access to Arm-NN-Functions
CMSIS-NN (external library imported before building)
Micro Interpreter
Operations resolver
Reference Kernel
CMSIS-NN Wrapper
Math
(standard lib)
CMSIS-NN
Kernel
(Interface)
CMSIS-DSP
Microcontroller device
(arm)
ML application with trained-model
Host (TensorFlow development Environment)
Builder
Build-Scripts
Compiler
(arm)
Executable
(.elf)
Debugger
(gdb-client)
Target
Debugger
(gdb-server)
Arm-ISS

## Slide 27: CMSIS-NN - Integration with TFL micro (Direct dependencies on CMSIS)
CMSIS-NN
CMSIS-DSP
Microcontroller device
Microcontroller files, i.e.:
Declaration of data-types needed by both the DSP and the NN libraries.
Function declarations for all DSP functions
Compiler-dependent definitions for special CPU-instructions, e.g.
  __SSAT
  __SMLAD
/* Implementation for Cortex-M0 and M3 */
for (i = 0; i < num_of_rows; i++)
{
int ip_out = ((q31_t)(bias[i]) << bias_shift) + NN_ROUND(out_shift);
for (j = 0; j < dim_vec; j++)
{
ip_out += pV[j] * pM[i * dim_vec + j];
}
pOut[i] = (q7_t) __SSAT((ip_out >> out_shift), 8);
}
/* If defined (ARM_MATH_DSP), takes the
* implementation for Cortex-M4 and M7
*
* An optimized implementation that used
* special instructions, e.g. __SMLAD which
* can perform two signed 16-bit
* multiplications.
*/
This is done similar for all functions under CMSIS-NN

## Slide 28: CMSIS-NN - An alternative approach for RiscV?
1. On Tensor-Flow side:
  Add wrapper for IFX’s CMSIS-NN
  Extend build system to
    Import CMSIS-NN library
    Build for RISCV
    Connect remotely to ISS
    Run acceptance tests provided by TensorFlow (e.g. kernel tests and interpreter tests)
2. On CMSIS-NN side:
  Set-up a base-repository an project structure
  Set-up development environment
  Start development and testing of kernel functions.
    Generic (it uses no Microcontroller-specific function)
    Optimized
Is it worthy to take advantage of the existing CMSIS-NN interface and implement it for IFX-RISCV, using as much as possible from the arm-implementation?
Micro Interpreter
Operations resolver
Reference kernel
Math
(standard lib)
CMSIS-NN
Kernel
(Interface)
NN-MATH
Microcontroller device
ML application with trained-model
Generic
Optimized
Generic
Optimized
CMSIS-NN Wrapper
This will require:

## Slide 29: CMSIS-NN - An alternative approach for RiscV?
TensorFlowLite Micro
Microcontroller-device (e.g. platform includes, linker)
Wrapping TFLu access to Arm-NN-Functions
CMSIS-NN (external library imported before building)
Micro Interpreter
Operations resolver
Reference kernel
Math
(standard lib)
CMSIS-NN
Kernel
(Interface)
NN-MATH
Microcontroller device (riscv)
HelloWorld_test
Host (TensorFlow development Environment)
Builder
Build-Scripts
Compiler
(riscv)
Executable
(.elf)
Debugger
(gdb-client)
Target
Debugger
(gdb-server)
ISS
(SweRV)
Although we want our CMSIS-NN implementation to be very similar to that of ARM, we also want:
To have a separate library instead of an extension of ARM implementation.
To be independent of CMSIS-DSP, which has many arm-dependencies and include much more from what is needed from CMSIS-NN
CMSIS-NN Wrapper

## Slide 30: CMSIS-NN - An alternative approach for RiscV? (The base-repository and project structure)
First, focus only on sources for cmsis_nn,
see https://github.com/ARM-software/CMSIS_5/tree/develop/CMSIS
Rename arm into ifxNN? Or just use arm prefix?
CMSIS_5
Version n
Do adjustments (setting precompiler defines) to compile the library for RISCV, as follows:
First, to support for the basic math-operations (e.g. *_fully_connected_q7)
Then, incrementally adding more complex nn-functions, e.g. *_convolve_HWC_q7_basic)
Fork CMSIS_5 repository into IFX_CMSIS
Version n+1
Update CMSIS_NN from community?

## Slide 31: CMSIS-NN - An alternative approach for RiscV? (CMSIS-NN structure and dependencies for IFX)
CMSIS-NN
NN-MATH
Microcontroller device
nn_math.h:
ONLY has to declare the data-types needed by CMSIS-NN.
Support GENERIC implementation:
  special CPU-instructions, e.g.__SSAT, shall be implemented in plain C.
nn_math.h
/* GENERIC implementation */
for (i = 0; i < num_of_rows; i++)
{
int ip_out = ((q31_t)(bias[i]) << bias_shift) + NN_ROUND(out_shift);
for (j = 0; j < dim_vec; j++)
{
ip_out += pV[j] * pM[i * dim_vec + j];
}
pOut[i] = (q7_t) __SSAT((ip_out >> out_shift), 8);
}
/* If defined (ARM_MATH_DSP), takes the
* implementation for Cortex-M4 and M7
*
* An optimized implementation that used
* special instructions, e.g. __SMLAD which
* can perform two signed 16-bit
* multiplications.
*/
Take the Cortex-M0 and M3 implementation as the default for any target

## Slide 32: CMSIS-NN - An alternative approach for RiscV? (CMSIS-NN structure and dependencies for IFX)
RISCV-V1
FullyConnectedFunctions
arm_fullyConnected_q7.c
In general, we could extend CMSIS/NN/Sources to include optimized implementations for different microcontroller variants, as illustrated below.
The build system, could then use a TAG to decide which function to include, e.g.
If TAG = RISCV-V1 then, arm_fullyConnected_q7.c shall be included instead of the reference implementation under CMSIS/NN/Source/FullyConnectedFunctions.
Any other nn-function will be taken from the reference-implementation.

## Slide 33: CMSIS-NN - An alternative approach for RiscV? (The development environment)
The development toolchain shall allow us to do the following:
Build CMSIS-NN source code and its acceptance-tests
Compile for different targets (e.g. host computer, riscV)
Debug on host-computer and on a target ISS (e.g. SweRV)
Develop and run CMSIS-NN’s acceptance-tests (on host computer and target ISS)
Develop and run unit-tests (on host computer and target ISS).
Perform static-code analysis, code-coverage report, etc
Generate documentation from source code (e.g. Doxygen)
Perform measurements on target ISS (e.g. memory footprint, run-time)
Continuous integration and continuous delivery
  EDEN? -> https://confluencewikiprod.intra.infineon.com/display/IFX/.What+is+EDEN+vv1.3.0
CMSIS-NN
NN-MATH
Microcontroller device
Acceptance-tests
Host (Our Environment to extend CMSIS-NN)
Builder
(SCons)
Compiler
(gcc, riscv)
Executable
(.exe)
Debugger
(GDB-Client)
Host
Computer
Target
Debugger
(GDB-Server)
ISS
(SweRV)
Build-Scripts

## Slide 34: CMSIS-NN - An alternative approach for RiscV? (TensorFlowLite Micro and RISCV-nn)
CMSIS-NN
NN-MATH
Microcontroller device
Acceptance-tests
Once everything is in place, we could start with the development, as follows:
On CMSIS-NN side (for every nn-function):
Modify CMSIS-NN sources (CMSIS_5 fork) until it compiles
Adjust NN-MATH functions to compile also for host computer
Adapt CMSIS-NN acceptance-tests to run on host-computer and ISS
Add first unit-tests
Adapt the implementation to pass unit-tests
Generate first documentation
Add first implementations of optimized-math-functions using RISC-V specific instructions
On Tensor-Flow side:
  Add wrapper for IFX’s CMSIS-NN
  Extend build system to
    Import/Download CMSIS-NN library
    Build for RISCV
    Connect via GDB to ISS
    Run acceptance tests provided by TensorFlow (e.g. kernel tests and interpreter tests)

## Slide 35: More info
TensorFlow Lite for Microcontrollers | TensorFlow
Get started with microcontrollers | TensorFlow Lite
Understand the C++ library | TensorFlow Lite
TensorFlow Lite converter | TensorFlow
TensorFlow tensors
TensorFlow Lite 8-bit quantization specification
https://nervanasystems.github.io/distiller/algo_quantization.html
https://github.com/google/gemmlowp/blob/master/doc/quantization.md#implementation-of-quantized-matrix-multiplication