## Slide 1
Convolutional layers optimization (Work in progress)
Jakob Kruse (IFAG DES SDF SCS SEM)
28.05.2020

## Slide 2
Conv Layer

## Slide 3: Convolutional layers
Convolve the filter with the image using dot product
Input_x
Input_y
Input_c
filter_x
filter_y
Input_c
equal
One output neuron

## Slide 4: Convolutional layers
Input
Output
Input_x * Input_y * Input_c
Out_x * Out_y * 1
Out_x = (Input_x – Filter_x + 1) / stride
Out_y = (Input_y – Filter_y + 1) / stride

## Slide 5: Convolutional layers
Input
Output
Input_x * Input_y * Input_c
Out_x * Out_y * n
Out_x = (Input_x – Filter_x + 1) / stride
Out_y = (Input_y – Filter_y + 1) / stride
Multiple Filters (n filters)
Batches not mentioned yet

## Slide 6: FLOAT Convolutional layer calculations
Computation is very similar to fully connected layer, with the difference that the weights and the input are 3-dimensional
Output size: (batch_size * out_x * out_y * out_channel)
Filter size: filter_x * filter_y * in_channel
For every output unit:

## Slide 7: UINT8 Convolutional layer calculations
Sum-of-filter-factor (with bias)
Always the same (can be precomputed)
Memory requirement: out_channel * int32
Sum-of-input-factor
Used multiple times (n=out_channel)
Should only be computed once
Not worth optimizing
New-input-factor
Must be calculated every time
For every output unit:
Reformulation of sum:
Finally, apply ouput shift, multiplier and offset and store value

## Slide 8: INT8 Convolutional layer calculations
ConvPerChannel function in internal/reference/integer_ops/conv.h is used!!!
Filter offset is assumed to be 0
Difference to uint8 implementation:
Precomputation of sum:
Sum-of-filter-factor (with bias)
Always the same (can be precomputed)
Memory requirement: out_channel * int32
New-input-factor
Must be calculated every time

## Slide 9: All optimizations I made
Dynamic memory allocation of OpData members
Moved CalculateOpData function call to Prepare phase
Precomputation of Sum-of-filters Factor
Precomputation of Sum-of-inputs Factor (not worth)
Loop variable optimization
Using filter consecutivity
Removing conditional statements
    Causes problems if dilation factor is not 1
     If dilation factor is not one, reference implementation is used
If padding != 0, the precomputation and filter consecutivity can‘t be used!
  Extra implementation in this case
  I added 2 extra tensorflow tests for padding (there were none)

## Slide 10: Benchmarks Int8
PO: Portable optimized
Optimizations:
  Precomputations(PC)
  Loop Variables(Loop)
  Filter consecutivity(Ficon)
  Remove Conditionals (nocond)
On host computer

## Slide 11: Benchmarks UInt8
PO: Portable optimized
Optimizations:
  Precomputations(PC)
  Loop Variables(Loop)
  Filter consecutivity(Ficon)
  Remove Conditionals (nocond)
On host computer

## Slide 12: Benchmarks RISC V
UInt8 | Reference | Port. Optimized
Avg Time | 3278 | 974
Int8 | Reference | Port. Optimized
Avg Time | 3602 | 1020
UInt8 | Reference | Port. Optimized
Avg Time | 3006 | 1229
Int8 | Reference | Port. Optimized
Avg Time | 3364 | 1089
With Padding (different values as above):

## Slide 13
Depthwise Conv Layer (WIP)

## Slide 14: FLOAT Depthwise Conv layer calculations
Output size: (batch_size * out_y * out_x * out_channel)
Out_channel = in_channel * depth_multiplier
Filter size: 1 * filter_y * filter_x * out_channel
One output neuron calculations:
The depthwise convolution convolves only one input channel for every output neuron (unlike the conv layer, which always convolves all input channels).
The 2D input channel is convolved with a 2D filter.
Every input channel can get multiple filters (depth multiplier)

## Slide 15: UInt8 Depthwise Conv layer calculations
Output size: (batch_size * out_y * out_x * out_channel)
Out_channel = in_channel * depth_multiplier
Filter size: 1 * filter_y * filter_x * out_channel
One output neuron calculations:
Reformulate sum:
=